Speed variation for the EUROCHAIN VL 10 hoist

As option, VERLINDE proposes speed variation of the hoisting movement for its EUROCHAIN VL 10 electric chain hoist. Intended for handling loads of 500 to 200 kg, it offers the user a high level of comfort together with highly flexible use.

Speed variation without fixed steps on the hoisting movements guarantees extremely precise positioning of the loads and more flexible use. Depending on the weight of the load, the type of movement and the experience of the user, he can adapt the travel speed as he wishes. The speeds are more reliable and precise; with a minimum speed close to 0.25 m/min (depending on the versions), it enables operators with less experience to handle loads without risk of damage.

| Configuration: -EUROCHAIN VL 10 standard chain-actuated electric hoist. -Encoder on drive shaft. -Braking resistance. -Brake control and rectifier relay. -Continuous speed control system. Enhanced productivity: Jerk-free starting, rapid accelerations and gentle halting speed up the handling cycles. Lower maintenance costs: Continuous control of speed enables electrical braking to be used as first priority during decelerations before actuating the mechanical brake (which wear by friction). The latter is used only as a holding (or parking) brake. |  |
| --- | --- |

Longer service life:

Thanks to progressive starting and gentler stopping, there are less mechanical shocks. The components of the hoist and the metal supporting structure are less highly stressed, thus also lengthening their service lives.

Low cost electric power supply:

Continuous control of speed makes for high electrical efficiency. In addition, the slow starting movement enables smaller power supply components to be used, calling for lower starting current.

Optimised safety:

A top and bottom limit switch and a load limiter are installed as standard equipment.

A speed supervision unit separate from the variator immediately stops all movement in the event of a difference in speed, overspeeding or jamming. If the motor does not rotate, or if a speed 20% above nominal sped is reached, the system stops all hoisting movement.

| Thermal protection of the motor: As standard equipment, the variator features thermal protection of the motor, based on measuring the temperature with thermistors encapsulated in the winding. Less maintenance: The motor is cooled by heat-exchange (insulation class F, protection IP 55). The hoisting chain is electro-zinc plated and calibrated for high strength (800 N/mm²). Compliance with standards: ENC levels. Release of electromagnetic radiation complies with standard EN 61800-3 A11 (2000). |  |
| --- | --- |

Elimination of all swinging of the load:

Combined with overhead travelling cranes or VERLINDE speed variation trucks, it also eliminates swing effects of the loads during combined lifting, travel and traversing movements.

A few figures on VERLINDE:

- the leading French builder and exporter of hoisting and handling equipment.

- the power of a group with a headcount of 5000

- a range of 30 hoisting products

- present in over 80 countries

- 10 sales agencies in France

- 24 after-sales service stations
- 9 cranes builders of EUROPONT-approved VERLINDE.